# Porsche Cayman S Headers Installation Guide

## Remove Factory Headers

Your Billy Boat Performance Exhaust system was designed to be a direct replacement exhaust system, while offering the best performance, finish and value available from a stainless steel exhaust system. Proper installation will ensure a lifetime of quality and performance from this product. If you have any questions please don’t hesitate to contact us.

You will need: Factory exhaust manifold gasket kit and WD-40

First, disconnect the NEG (-) battery terminal.

Lift rear of car and support in appropriate locations with jack stands (consult owner’s manual), set emergency brake and chock wheels. Note: factory mounting configuration – installation of the B&B Performance headers is simply the inverse.

Begin to remove the factory header by removing the (6) bolts holding the primary flange and the (3) nuts holding the secondary flange together. After all hardware is removed work the headers off one side at a time. It may help to saturate mounting points and hardware with WD-40 to penetrate corrosion.

## Install your new Porsche Cayman S Headers

With the factory headers removed, inspect the original gaskets. They are reusable, however use your best judgment, now is a good time to replace them with new factory gaskets. Re-install headers to cylinder head.

Start the car and listen for any exhaust leaks or rattles. After ensuring that there are no leaks or rattles go for a drive and listen for rattles over rough surfaces. After 500 miles re-torque your work to ensure all mounts are secure.